## Slide 1: analysis of charging schedules of electric vehicles considering end-user inputs
Presented by :
Arudpiragasam Krisnaragavan - 3105647

## Slide 2: Contents
01
02
03
04
DLM with Scheduling
Introduction
Data Analysis
Problems Statement
04
05
Benefits

## Slide 3
Introduction
Necessity of Smart Charging
IC vs EVs

## Slide 4
Factors influencing customer
Orientation of charging station
Maintenance
Cost
Availability

## Slide 5
Data Analysis
The peak Power consumption
  Monday: 1128.88 kWh
  Tuesday: 1011.32 kWh
power consumption peaks range between 8 am and 4 pm
Analysis of power consumption(kWh) for each year
Analysis of power consumption(kWh) for each day

## Slide 6
Data Analysis
The stations E12, E11 and E13 are having higher power consumption than the rest of the charging stations
Analysis of Power Consumption for Each Charging Station
Analysis of Total Power Consumption for Each Charging Station

## Slide 7: Problem Statements
The stations are overloaded from 8 am to 4 pm and this significantly increases the cost of charging and overburdens the grid
During the working days, the power consumption is higher compared to that of the weekends
The charging stations are not used simultaneously, and each station has different power consumption
Few of the most used stations are active only during working hours and bare a large power consumption in these hours
Few of the stations has minimal power consumptions or some time no power consumption during the non-working hours
Few stations are more popular than most of the stations and are being used regularly

## Slide 8: Dynamic Load Management With Scheduling
State-1
State-2
State-3
State -1: Off-Peak (12 am – 8.59 am)
State -2: Peak (9 am – 4 pm)
State -3: Off-Peak (5 pm – 11.59 pm)
Fig: Total Power Consumption vs Time

## Slide 9: List of abbreviations
DLM - | Dynamic Load Management
EP - | Emergency Power
PS - | Prediction Slot
NS - | Number of Charging Slot
P - | Peak Power
AP - | Available Power
CP - | Calculated Power
SOC - | State of Charging
Emergency charging Price = 3 * Normal Price
Peak Time
Charging Price = 2 * Normal Price
Off-Peak Time
Booking Slot = (CS-PS )*75%
Charging Price = Normal Price
Fig : DLM With Scheduling

## Slide 10: Benefits Of DLM With Scheduling Strategy
Prioritizes the vehicles need to be charged based on the EDF (Earliest Deadline First)
This strategy can be implemented in the existing charging stations to avoid any further addition in the infrastructure
The charging costs for customers can be reduced
The electricity costs can be maintained in economical ranges by evenly distributing the power consumption throughout the day hence reducing the peak time costs
Reduces the stress on the grid without overloading the grid by filling the valleys of power consumption
The customer could schedule their EVs according to their priority and Utility owners can benefit by charging higher prices for higher levels of priority

## Slide 11: Hybrid Power Cost Estimation
Cost estimation for Solar Panel |  |  | 
Per panel cost ( Euro ) | Rated power ( W ) | Unit Charge ( €/W ) | Cost of Solar panel ( Euro )
24 | 335 | 0.764/watt | 256
Battery Size | Charging Time | Cost per kW (€) | Cost to fully charge
24 kWh Battery | 30 min | 0.18/kW | € 4.3
Consumer Charging Cost
Website and App Cost per Month | Dynamic Load Management Cost Per month | Station Maintenance cost Per month | Parts and Labor cost Per month | Total cost
€ 14 | € 2,500 | € 30,000 | € 50,000 | € 82514
Infrastructure Expenditure

## Slide 12: References
Joosung Kang, Scott J. Duncan, Dimitri N. Mavris,” Real-time Scheduling Techniques for Electric Vehicle Charging in Support of Frequency Regulation”, Georgia Institute of Technology, Atlanta, GA,March 19-22, 2013.
Yunjian Xu, Feng Pan, Lang Tong,“Dynamic Scheduling for Charging Electric Vehicles: A Priority Rule”,February 1,2016.
YONGMIN ZHANG,” Dynamic Charging Scheduling for EV Parking Lots With Photovoltaic Power System”,October 1,2018.
Zechun Hu, Kaiqiao Zhan, Hongcai Zhang, Yonghua Song,”Pricing mechanisms design for guiding electric vehicle charging to fill load valley”,2016.
Zhe Yu, Yunjian Xu, and Lang Tong,” Large Scale Charging of Electric Vehicles: A Multi-Armed Bandit Approach”,May 17,2016.